## Slide 1: Physical Security – the Good, the Bad, and the Ugly Mark Seiden MSB Associates m@seiden.com
Notes: No matter what battles have been won or lost in information or network security, there is still the bedrock requirement for physical security without which it is impossible (I assert) to have any sort of meaningful confidence in the quality of your other kinds of security.
So this talk will serve as a tutorial, or perhaps a collection of mini-rants on various aspects of physical security, but treated from an information security perspective.
(abstract)

## Slide 2: What is physical security, anyway?
Access to tangible assets or artifacts that represent them or access to them.
Example of such assets include
people, computers, network plugs, the phone switch, a sysadmin’s keyboard interface, unencrypted backup tapes, the encryption keys on a floppy disk, the list of code names for the deals in play, the personnel database, the access control computer on the enterprise net, the master key in the coffee cup, a clear view of the safe dial, the bearer bonds in the safe.
Rather than attempt a rigorous definition, it’s more fun to define it contextually… but as programmers, let’s try to do it top-down.
Notes: We are programmers, after all, so should we prefer to develop the definition top down, or bottom up?
Let’s go for top-down.

## Slide 3: Physical security on Planet Earth
Perceptions about security has been elusive and highly distorted since 9/11.
One can’t economically “secure” anything large against a determined adversary with substantial resources.
People are not rational when making risk vs. reward or investment decisions. Politicians (= sales people) use the “fear sell”.
Little evaluation of effectiveness of controls -- public perception and the ability to grab land are key.
Rights to (and value of) “identity” and “privacy” are still in gray areas in many countries.
Notes: I can’t solve these problems in an hour at Usenix, so let’s go down a level:

## Slide 4: Physical security in the business environment
Some nasty trends reduce security (particularly control and auditability)
Offshore development and operations (particularly customer service)
Outsourcing to external entities
Centralization of control and operations often = Making the wires much longer than ever
Notes: Moving all of this offshore means your code and your data are both at risk to people you might have less trust in, and who might have less stake in your success than your own employees.
Outsourcing in general is a disaster for security. You substantially lose control over the way in which work is done to accomplish some goal. Not only do you trust the outsourcer, but all of the outsourcer’s outsourcers. You have very little visibility into the process, and can’t say “no” unless contracted service levels are unmet.
What can you practically outsource? Some companies are outsourcing their email to companies that scrub it for spam. That this means the company’s employees can read the email
Some companies outsource their backups, on several levels. The backups might be done across the net, or the physical backup tapes might be taken by a courier unknown to them to an offsite storage site they’ve never seen.
Some companies outsource their entire networks, or their server infrastructure.
Some companies outsource the production of their ID cards and the operation of their card access control system.
Companies often hire guard services or alarm companies. Companies often outsource their voice comm infrastructure.
Later I will go over some case studies in outsourcing, but meanwhile, let’s go down another level, and talk about physical security in a typical large enterprise, perhaps with a campus or multiple campuses.

## Slide 5: Physical Security in the Enterprise
Fragmented responsibility and authority (split among facilities, sysadmin, networking, legal, HR, vendors), often multi-site.
Shoestring budget, particularly for remediation of older facilities
If there’s “risk management” at all it’s often got an insurance mindset
Those with functional power are often low status, low skill, low training and quaity of their work is seldom measured or rewarded, so taking shortcuts is common.
Decisionmakers have neither the time nor skills to verify vendor claims, and almost no solutions are “open source”.
…and they strongly believe in Security Through Obscurity.
Notes: Many of these comments apply to security in general

## Slide 6: …
Common copouts, rationalizations, excuses:
“That’s not my job” or “It’s my vendor’s problem”.
“I don’t consider that a plausible threat” or “We’ve never had that problem before”.
We just have to raise the bar enough for them to go somewhere else.
Our controls are better than locks and keys.
You have to trust x or they won’t get any work done.
But that database is encrypted!

## Slide 7: Physical Security in a campus or building
There’s a lot of “legacy” to deal with in pre-existing buildings not specifically designed with security in mind
Existing partial-height walls, hung ceilings and raised floors, wiring rooms in the wrong places, wire runs through public areas, unsegmented networks, already installed doors and locks.
Is there any perimeter? (At least we can still ask that question in physical security).
Is there any protected area/vault which can serve as a basis for trust?
Can one safely provide friendly facilities for joint venture partners or visitors?
Required backdoors or key escrow (e.g. “Knox Box”).
Building control (Local Operating Networks) (e.g. LONworks).
Notes: Are alarms integrated with access control?

## Slide 8: Multi-tenant buildings weaken the defensible perimeter
Shared infrastructure: telecom, datacomm, cleaning/janitorial facilities, common areas which are likely to be weak or unprotected.
Probably master keyed
Unknown visitors and deliveries to other tenants
Independent access policies and controls
It’s ifficult to secure “the building” as a whole (on any level).
The weakest tenant’s security policy could become your de facto security policy.

## Slide 9: Colocation facilities are a very special case of multi-tenant buildings
Some are like “gated communities”.
Others are more like campgrounds with video.
Your co-tenant’s weakest visitor and vendor policy puts you at risk.

## Slide 10: And finally we get down to the ground level components – nuts and bolts
Or, in this case, such elements as
Locks and electronic access controls (cards, readers, biometrics)
Sensors and alarms
Auditing facilities (to figure out what happened) such as
Video surveillance, backups, telephone detail billing, badge access logs.
These components have complex Real World interactions.

## Slide 11: Doors
Made of?
Single or double?
Double glass doors usually have a gap between them. What’s within reach?
Where and of what construction are the hinges?

## Slide 12: If doors are simple, how can they go this wrong?

## Slide 13: …

## Slide 14: Locks
Tubular, Rim or mortise
have different latch designs, different force-resistance, varying reliability, and weaken the door more or less.
Mechanical, possibly with electric strike, or Electrified
And there’s an access control, a “lock cylinder” in which you put a “key”, (perhaps a reader for a badge, perhaps a biometric device or pin pad.)

## Slide 15: Problems with Locks
Sometimes you can’t easily tell by looking if they’re locked or unlocked
Deadlockers are often mis-installed, broken, or ineffective
Keyed locks often permit bypass on doors controlled by badge access control or a numerical code

## Slide 16: Request-to-exit switches

## Slide 17: How do you get out, then?

## Slide 18: Frameless glass doors are a problem

## Slide 19: Request to exit sensors
Usually passive infrared (sense temperature differences between an object and the background)

## Slide 20: Problems with Strikes (Electric or Magnetic)
The biggest selling tubular locks have deadlockers rendered ineffective by the biggest selling electric strikes

## Slide 21: …
Exposed/accessible strike placement or wiring
Magnetic strikes not on uninterruptable power
Magnetic strikes are frequently on the wrong side of the door
Adhesive tape on magnetic strike reduces holding strength dramatically (according to an inverse cube law!)
Magnetic strikes need a request-to-exit sensor or switch

## Slide 22: And problems with lock cylinders…
Picking
Making a key, or even better a master key.
On Interchangeable Core cylinders, making a Control Key, which allows easy removal of the lock cylinder and replacement with one of your preference.
Very few lock instances are necessary for a brief time to make a master or control key by disassembly. Locks in public areas, old doors in basement storage, and padlocks frequently/easily sprout legs.
Revocation of rights is unacceptably difficult and expensive with mechanical locks.

## Slide 23: Electronic access controls
There’s a computer and a database involved (oh oh).
It’s wired (somehow) to microcomputer-based “panels” with local authority to unlock doors (containing caches of access rights and access events.)
Panels are connected on local wiring (a loop or point-to-point) to badge readers, electrically-controlled locks, door state sensors and “request to exit” sensors or switches. Lots of components which can be manipulated along long wires!
A refreshing number of ad-hoc proprietary protocols to look at. Any bets how frequently these components mutually authenticate their counterparties in a authentication or auditing transaction?
Back doors for installers and maintainers (and maybe others).
Notes: Explain “request to exit”.

## Slide 24: And what about those cards?
Proximity cards are an early example of RFID tags.
Typically have a short facility ID and a card number (think of a subnetted 32-bit IP address).
Most can be read remotely by an attacker (no challenge’/response0 -- imagine a card emulator that will replay the bit sequence just read.
Some are “field programmable”
Low card numbers are often more senior = more privileged.
Brute force attacks are typically logged but there are no countermeasures
So are these more or less secure than keys? Instant revocability and fine-grained access control are their big advantages, but a class attack makes them risky.

## Slide 25: A case study (Mark Seiden/Mark Chen)
Receptors GP3 access control system.
SCO Unix on a PC on the enterprise network but with nonstandard addresses. Serial wiring to “guard stations” running terminal emulation, TCP to ethernet-attached panels.
Root password (“r00t”) published in the user manual.
Dialup modem (which tech support recommended be always left on).
So I logged on as root, and started poking around.
Netstat –na said it was listening for tcp connections on 21 ports including rexec, rpc, and sqlexec.
All the source was on the machine and features were compiled in with #defines. (e.g. #ifdef JETWAY, #ifdef US_HOUSE)

## Slide 26: …
customers mentioned in the source code (with #ifdefs) included
LDS CHURCH, AMD, GE King of Prussia and Camden, University of Washington, Corning, US House of Representatives, US Senate, USC, Yale, and 5 airports by name.
(Turns out their customers included >50 airports, prisons, courthouses, and even a spook agency.)
Looking at the database schema and tables was instructive!
The system has a concept of “passkey”, a magic word typed at a guard terminal which conveys various privileges. (all in database table psky.dat, lightly obfuscated).
Looking at the passkey validation code, we noticed that there was a special undocumented passkey, a magic function of the date, which conveyed system manager privilege to anyone knowing the magic spell.

## Slide 27: So, what could an attacker do?
An outsider on a dialup line, or an insider on the LAN, could
permanently or temporarily enable badges with bogus access or deny access to legitimate users.
cause immediate diagnostic events to occur (e.g. unlocking doors or areas),
schedule timed events to occur (e.g. unlock all doors 2am-3am on Sunday)
create stealth badges (which then had unlogged access).
alter unsigned code downloaded to badge controllers (stored on the UNIX host).
Disable the logging/history mechanism, remove or alter log records in the database.
Notes: Stealth badges were supported due to a bug in logging. An event caused by a badge not in the user table was ignored (rather than treated as an alarm event).

## Slide 28: Sensors and alarms
When is sensed movement in a protected area an alarm event? One solution is forcing everybody to badge in and out, and reference-counting the occupants. When the count is 0, nothing should be moving.
But alarms are usually dis-integrated from badge systems, which makes this difficult to impossible.
Sensors can sometimes be activated from outside the protected area. This can be used to cause false “request to exit” events or nuisance alarm conditions. (False alarms are a social engineering opportunity).
Sensors are wired to their control elements in primitive ways (usually a closed loop).
Battery-powered Wireless sensors. Think “garage door opener” technology. Battery consumption has traditionally been more important than security.

## Slide 29: Video
Cheap USB- or net-connected digital motion-detect video compensates for a wide variety of sins, (or the temptation to sin by unknown third parties).
Video can go almost anywhere these days, in things that look like or started life as floodlights, smoke detectors, clocks, pagers, or eyeglasses.
But…
You need to provide adequate coverage of asset areas (image size, illumination, numbers of cameras) and in the time domain, too.
You need random access and adequate retention to be able to follow up..
You need to carefully control access to the stored video.
Bad guys can make use of video also!

## Slide 30: A colocation case study
Very large facility with “vaults”, cages, and cabinets on a raised floor.
Common data wiring is in conduits overhead. Raised floor is plenum for cool air and power. (Heat is not your friend.)
Facility issued their own anonymous looking prox card credential.
Cabinets with wafer locks in common areas (not even in cages)
Cages had 5’ coarse mesh walls, video in some of the aisles, masterkeyed sliding doors, could be easily opened using several methods.
“Vaults” had video pointed at the door, hand geometry readers for entry, electrified lock, a “door open” magnetic switch, a motion detector just inside the door.

## Slide 31: Need some concept of Identity for most controls to work effectively
Perhaps they need to know who you really are
Or more likely just that you are the same person as registered before.
Or, best of all, that you have particular roles or rights (the right to drive, or to drink, or to go into vault 203 unaccompanied.)
We have been conflating these aspects of identity, devaluing our identity documents by leaking stronger authenticators to counterparties even for low value transactions.
Is it better for your colo to accept your driver’s license, to issue you their own credential containing a shared secret or to check your face in a database?
Notes: Drivers license for prepaid hotel rental in Portland
Passport for hotel check in in Spain

## Slide 32: Events of a single month pointing to identity theft as a growth area
Brooklyn, New York: busboy targets Fortune “400 richest”.
Verisign issues two Class 3 code signing certificates in the name of Microsoft Corporation (perhaps to a Brooklyn busboy.)
US General Accounting Office reports assault weapons and ammunition easily obtainable using phony driver’s licenses (GAO Report 01-427)
Notes: From Forbes:
Two New York City men allegedly stole the identities of the United States' wealthiest people through the Internet and tried to funnel up to $30 million from their bank accounts, according the New York Post. The suspects, Abraham Abdallah, 32, and Michael Puglisi, 47, were foiled when they attempted to steal $10 million from the account of an unidentified tycoon. The Brooklyn duo apparently targeted members of the Forbes 400 Richest in America, including Microsoft co-founder Paul Allen and media mogul John Kluge, who they thought would not notice the disappearance of $1 million dollars, according to the story. (and there’s a particularly ironic link to the 400 Richest). It’s not that hard – “Edgar Online” has Paul Allen’s social security number visible to anyone who looks.
From the GAO report:
The five states that we selected to purchase firearms in—Virginia, West Virginia, Montana, New Mexico, and Arizona—conformed to the Brady Act's minimum requirements, relying on an instant background check.
They do not have additional requirements for fingerprinting or waiting periods…. we created counterfeit state driver's licenses for the five states with fictitious names, dates of birth, and/or social security numbers using off-the-shelf software, a scanner, a laminator, and a color laser printer. Two special agents acting in an undercover capacity used the counterfeit driver's licenses in attempts to purchase firearms from gun stores and pawnshops that were licensed by the federal government to sell firearms in the five selected states. We selected these gun stores and pawnshops at random from the yellow pages of local telephone directories…. in the five states we found that the instant background check does not positively identify purchasers of firearms. Rather, it is a negative check that cannot ensure that the prospective purchaser is not a felon or other prohibited person whose receipt and possession of a firearm would be unlawful. Similarly, in one state— Virginia—the additional step of requiring a state criminal history check was also a negative check.
Well, there is some process involved: You fill out a form.

## Slide 33: A system that keeps honest people honest?
Notes: On BATF form 4473,
Answering such questions as d “are you a fugitive from justice”, e “are you an unlawful user of or addicted to drugs”, and “have you ever been adjudicated mentally defective?”

## Slide 34: Everything you need to create identity is available on Ebay!

## Slide 35: Santa Fe, New Mexico Purchase
Notes: Supply the phone driver’s license, and 24 hours later… you can have something like this…
Interesting, the things we can buy with phony identification.

## Slide 36: While we’re showing scary devices
Notes: Keyghost. $89, for 128K char capacity. Capacity up to 2MB. That’s a year of your typed secrets. There are even versions which lives quietly inside a PS2 keyboard, for around $150, There’s an equivalent device called Keykatcher which is only $59 (including shipping) for 32k characters.
if you don’t like hardware, I can count approximately 30 software utilities that do keystroke logging. Some will even email you the log. I can’t more persuasively demonstrate to you the ineffectiveness of passwords or passphrases than to show you these gadgets. Are biometrics any better? That depends on how sniffable they are.

## Slide 37: We knew about electromagnetic emanations
But what about acoustic emanations?
Dot matrix printers
Keyboards, telephone keypads, ATM Pin Pads
Dmitri Asonov, Rakesh Agrawal:

## Slide 38: Feature extraction from the acoustic signal
Trained a neural network…

## Slide 39: Asonov and Agrawal’s interesting findings
Average Depth of Correct Symbol (for 30 keys) is 1.99. (9,0,0) means neural network output this key 9 times as first choice, 0 times as second choice, 0 times as third choice. The same keyboard was used for training and testing.

## Slide 40: …
Asonov and Agrawal also have less dramatically demonstrated successful acoustic recognition of ATM PIN pads and telephone keypads.
What solutions?
Don’t use keyboards with acoustic outputs during PIN or password entry (one patent they cite suggests eyetracking is a good solution).
Mute telephone microphones during such entry.
Don’t use passwords at all (although replay attacks are still problem with tokens.

## Slide 41: Unauthorized 802.11 bridges are pretty scary also.
They can (lightly) encrypt and leak your traffic outside your building
They’re cheap
They require only brief access for bad guys to install them

## Slide 42: Problems with Credit and Debit Cards
Notes: Credit cards never worked well with Mail Order/Phone order. So they added the CVC and CVC2 values as secondary verifiers.
Chip cards are rare in the US. Anyone know why they’re common in Europe?
Because the phone network is considered inadequately reliable, they needed a way to do offline verification of each card.
The global credit card companies are finally realizing the “skimming” is a big problem, more than US$ 1Billion per year.
The biggest problems at the moment are specially instrumented ATMs that capture card data and PIN data, using, for example, “parasite” card readers, along with video cameras or keypad overlays, and reports of non-bank ATMs with modified software.

## Slide 43: Systems of all sorts are decreasingly
Designed
Built by people who truly understand their behavior
Deployed by such people
Tested
This is as true for security systems as for the buggy applications we are in such a hurry to expose to our customers.
Notes: We’re seem in too much of a hurry to think about what we’re about to be doing. Time to market is considered very important. As security consultants, we’re often called in at the last minute, almost as an afterthought.
The commodification of programming and the many levels of abstraction between us and the machine or the bits on the wire mean we no longer really know what those layers are doing. Instead we use middleware, off the shelf software, or whatever to get the job done with as little programming as possible.
So the people who deploy or operate the systems don’t know how they were built. Even the programmers often have moved on to other projects. Did they leave back doors in the code? The recent case of Interbase is instructive. It had a back door in it for 7 years, that allowed any local or remote user to manipulate any database object on the system. If the database server ran as root, this would allow the user to do anything. The back door was controlled by a fixed, easily located, unchangeable password, stored as plaintext in the binary. The only way this was discovered is some months after the system became open source. The database login was “politically” and the password? “correct”.
This happens too often. Last year, there was a back door password in a shopping cart system “cart32” that had been there for 5 years. How’s a user expected to find such things? Through testing? Through reverse engineering?
These days, testing is left to the users.
ALPHA: Software undergoes alpha testing as a first step in getting user feedback. Alpha is Latin for "doesn't work."
BETA: Software undergoes beta testing shortly before it's released. Beta is Latin for "still doesn't work."

## Slide 44: Scary trends
All your secrets on your laptop
Or maybe: all your secrets on your Palm Pilot
Or maybe: all your secrets on your converged wireless phone/palm pilot/remote control/electronic wallet (“trust us, it works”)
Notes: Thus, people will try to keep all their secrets on their laptops, or perhaps on their Palm Pilots.
If you lose these devices, chances are you lose your secrets. There has recently been an entertaining tendency for members of MI5 and MI6 to lose their laptops in pubs or airports, and you may recall in April, 2000 the loss of a laptop containing arms secrets from the State Department Bureau of Intelligence and Research (INR), supposedly one of the most secure bureaus at the State Department.
The laptop held several thousand pages of "code word" documents on the sources and methods of what the State Department calls "proliferators" of weapons of mass destruction, nuclear, chemical and biological. It wasn’t protected by passwords or encryption.
In May, it was pointed out that approximately 550 “media representatives”, including 67 foreigners had 7*24 unescorted access to the State Department building.
In August, the govt offered a $25k reward for it, having not yet found it! In December, they disciplined a number of people over the incident. According to an e-businessworld story:
“State Department official who spoke on condition of anonymity said the security procedures put in place to date are taking their toll on the agency. "We are so tied in knots about security here, it is amazing we can do anything," the official said.
Stephen Aftergood, an intelligence specialist at the Federation of American Scientists in Washington, called the State Department's actions "heartbreaking" and said there should be a better way to handle these situations. "We are running the risk of creating a secure workplace where no one wants to work," said Aftergood.
Allen Thomson, a longtime CIA veteran, called the State Department's response to the missing laptop, as well as the CIA's recent firing of four employees for taking part in an unofficial chat room on CIA data networks, symptoms of "[Wen Ho Lee]-induced cybersecurity hysteria." Lee is the Taiwanese-American scientist charged by the government with downloading nuclear secrets from computers at the Los Alamos National Laboratory in New Mexico.”
More than 300K laptops were stolen in 1999 alone.

## Slide 45: Vendors are often in league with the devil
“In memory of Ellen Shannon Aged 26 Years
Who was fatally burned March 21st 1870
By the explosion of a lamp filled with R.E. Danforth’s
Non Explosive Burning Fluid”
-- tombstone epitaph, Girard PA.
Contractually require audits, independent design and code reviews, employee security as rigorous as your own, and prompt disclosure of all flaws in products and services.
Notes: Remember that $25k reward? Lucira, a local company, decided to add $50k to the reward. Probably thought it was cheap publicity.
What do they make? A Laptop tracking program. How does it work?
“ …Our software stealthily resides on your PC with minimal configuration in a manner that is
virtually undetectable. Once installed, Lucira's Tracking Solution will be virtually impossible to remove without your authorization. Each time your PC signs-on to the Internet, Lucira's Tracking Solution checks against a list of stolen PCs to determine whether it has been reported stolen. If the PC has not been reported stolen, Lucira's Tracking Solution does not transmit any location information to Lucira Security Central™. If, however, the application discovers that the PC has been properly reported stolen, it silently transmits location information to Lucira Security Central™, using a combination of patent-pending IP and telephony technologies. After receiving proper authorization from the PC's owner, Lucira will furnish this location information to local law enforcement, facilitating prompt recovery of your hardware.”
Do I believe it works? Only against relatively stupid thieves. How do they keep it from being removed from the hard drive? Well, as it says in their press release “SecurePC(TM) is undergoing final Beta Testing at the Massachusetts Institute of Technology. “tc

## Slide 46: “She blinded me with science”
But do you really think science will protect you?
The “people problems” are most difficult:
Social engineering
Passwords
Trust of insiders
The building master hidden in the coffee cup of the facility manager who was too low status to have a locked office
People resist heavy-handed authority
People will cover up even the most severe incidents. For example, the loss of a complete set of keys.

## Slide 47: Some rules of thumb to avoid “physical security hell”
Just as in information security:
You need to understand your business assets and plausible threats to them
The risks are yours, and (no matter what) it’s your reputation on the line, even if you can shift the formal liability elsewhere
It’s usually cheaper to create compensating controls to detect problems than to prevent them in the first place. This is where a bit of obscurity can add value.
You need to put some policy and process in place and verify that the policies are dynamic, culturally appropriate, and reasonable.

## Slide 48: …
Design and architecture are very important, and you can’t do them economically late in the game, even less so when bricks and mortar are involved.
“God is in the details” – put someone on your side who really understands them and who can help you keep things clean.
Audit your vendors. Test the locks. Test the manual procedures. If you want to be considered a good guy by your vendors, hire a consultant to act like a bad guy and to provide plausible deniability.

## Slide 49: …
A healthy level of paranoia can be a good thing.
For many things “trust but verify” is a good practice. This means independent verification rather than relying on vendor representations or self-certification.
Use secret-sharing or other multiple-custody protocols for key installation.
Know who you’re trusting.
Pre-employment background and credit checks for sensitive employees including those at your vendors.
Notes: You can’t trust your vendors, or your insiders.
Bad guys, inside or outside, will find the weakest link and exploit it.

## Slide 50
"Knowing is not enough; we must apply.
Willing is not enough; we must do."
-- Goethe (1749-1832)

## Slide 51: References
“I can copy a proximity card at least as easily as I can take an impression of a key.” -- Jonathan Westhues http://cryolite.ath.cx/perl/skin/prox
Keyboard Acoustic Emanations (Dmitri Asonov, Rakesh Agrawal)
www.almaden.ibm.com/software/quest/Publications/papers/ssp04.pdf
Matt Blaze on makins Masterkeys: www.crypto.com/masterkey.html
And on safe cracking: www.crypto.com/papers/safelocks.pdf
Securitech Gallery of {illegal, badly locked doors} off www.securitech.com
Questions: Now or later to m@seiden.com
(and thanks for listening)

## Slide 52: Barry Wels references
Opening locks by bumping paper:
Wwwtoool.nl/bumping.pdf
Winkhaus press release responding to vulnerability disclosure
www.winkhaus.de/presseframe/files/041014_Statement_Presse_BlueChip.doc