## Slide 1: Wikipedia: Edit This Page
Differential Storage
Tim Starling

## Slide 2: Wikipedia Growth
Wikipedia and related projects have been growing at a phenomenal rate
Database size doubles every 16 weeks

## Slide 3: MediaWiki Design
Based on the principle that hard drive space is cheap
Minimal development time
Each revision stored separately
  Completely uncompressed until January 2004
  Revisions now compressed with gzip for 50% saving
Everything stored in MySQL – copy of every revision on every master or slave machine
Notes: http://sxc.hu/browse.phtml?f=view&id=191618

## Slide 4: Hardware Requirements
Master DB server: ariel
Worth $12,000
Dual Opteron, 6x73GB 15K SCA SCSI drives: 4 RAID 1+0 (146GB), 2 RAID 1 (72GB)
Effective capacity 200 GB
Database size 171 GB
No more drive bays available
Only a week of growth left

## Slide 5: Differential Storage
Why not store diffs, instead of complete revisions?
Canonical example: RCS
1.71
1.70
Current revision stored in full
1.69
…
Diff
Diff
Other revisions calculated on demand

## Slide 6: Differential Storage
RCS:
  is designed to store code
  has a simple ASCII data format
We want the best possible compression ratio
No need for readability
Can we do better than RCS?

## Slide 7: Wiki Compared to Code
Wikipedia articles have long lines, many minor changes are made
Better if we don’t have to duplicate the whole line
Notes: http://en.wikipedia.org/w/wiki.phtml?title=Greenwich_Hospital&curid=337381&diff=0&oldid=0

## Slide 8: Wiki Compared to Code
Some articles have lengthy “edit wars”, where the article alternates between two significantly different versions.
Can we store this efficiently?
Notes: http://en.wikipedia.org/w/wiki.phtml?title=Mother+Teresa&limit=50&offset=300&action=history

## Slide 9: Efficient Differential Storage
What if someone moves a paragraph from one location to another? An ordinary diff won’t store that efficiently.
12,13d11
< [[Image:AndalusQuran.JPG|thumb|right|280px|[[12th century]] [[Andalusia]]n Qur'an]]
<
17a16,17
> [[Image:AndalusQuran.JPG|thumb|right|280px|[[12th century]] [[Andalusia]]n Qur'an]]
>

## Slide 10: The LZ Connection
What we need is an algorithm which will recognise arbitrary sequences of bytes in one revision which are repeated in another revision, and then encode them such that we only store the sequence once.
This just happens to be what compression algorithms such as LZ77 do.

## Slide 11: New Storage Scheme
Concatenate a number of consecutive revisions
Compress the resulting “chunk”
A good compression algorithm will take advantage of the similarity between revisions, and achieve very high compression ratios

## Slide 12: Proof of Principle
We compressed history of three articles:
  [[Atheism]], an article with lots of edit wars
  [[Wikipedia:Cleanup]], a discussion page which is incrementally expanded
  [[Physics]], a typical article with a long revision history
Because all these articles have a very long revision history, we would expect better than average compression ratios

## Slide 13: Proof of Principle
Size of the compressed text compared to the original text:
As expected, diffs performed poorly in the edit war case, but very well for incremental addition of text
Compression methods always performed well

## Slide 14: Gzip, Bzip2 and Diff
Other tests showed bzip2 to give better compression than gzip, but at a much slower speed
Ratio for diff could have been improved by choosing the most similar revision to take a diff against
Diff much faster than gzip or bzip2
Diff-based compression is harder to implement

## Slide 15: Implementation
We implemented a gzip method in MediaWiki 1.4
Compression is taking place as I speak
Expected effects:
  Better utilisation of kernel cache
  Higher I/O bandwidth for uncached revisions
  Smaller DB size
Average compressed size: ~15% of original
Higher than the tests because the tests used articles with many revisions

## Slide 16: Future Directions
More detailed evaluation of diff-based methods
Other ways to solve the space problem:
  Application-level splitting across distinct MySQL instances
  Distributed filesystems, e.g. GFS