## Slide 1
Building Systems on Your Own Soft Core
OR
Blurring the
Hardware / Software Interface
Klaus.Schleisiek AT freenet.de
www.microcore.org

## Slide 2: Topics
Architecture
Opcodes
Co-Design Environment
Debug Environment
Geolon-MCS (a concrete product)
Interrupts and Exceptions
Special Instructions
Scalability
Prototyping Board
Licensing
Next Steps

## Slide 4: uCore Architecture
Dual Stack
  Forth oriented instruction set
Harvard
Prefix Code (Transputer Style)
  Scalable data width
    Object code compatibility
Interrupt
  after every instruction
Exception
  hardware mechanism for multi tasking

## Slide 5: uCore 1.20 Opcodes by Functionality
  NEVER NONE BRA Op: nop ( -- )
Unary Operators
  NOT BOTH ALU Op: invert ( n1 -- n2 )
  SL BOTH ALU Op: 2* ( n1 -- n2 )
  ASR BOTH ALU Op: 2/ ( n1 -- n2 )
  LSR BOTH ALU Op: u2/ ( n1 -- n2 )
  ROR BOTH ALU Op: ror ( n1 -- n2 )
  ROL BOTH ALU Op: rol ( n1 -- n2 )
  ZEQU BOTH ALU Op: 0= ( n1 -- flag )
  CC BOTH ALU Op: cc ( -- )

## Slide 6: uCore 1.20 Opcodes by Functionality
Binary operators
  ADD POP ALU Op: + ( n1 n2 -- n1+n2 )
  ADC POP ALU Op: +c ( n1 n2 -- n1+n2+carry )
  SUB POP ALU Op: - ( n1 n2 -- n1-n2 )
  SSUB POP ALU Op: swap- ( n1 n2 -- n2-n1 )
  AND POP ALU Op: and ( n1 n2 -- n1_and_n2 )
  OR POP ALU Op: or ( n1 n2 -- n1_or_n2 )
  XOR POP ALU Op: xor ( n1 n2 -- n1_xor_n2 )
  ADD PUSH ALU Op: 2dup + ( n1 n2 -- n1 n2 n1+n2 )
  ADC PUSH ALU Op: 2dup +c ( n1 n2 -- n1 n2 n1+n2+carry )
  SUB PUSH ALU Op: 2dup - ( n1 n2 -- n1 n2 n1-n2 )
  SSUB PUSH ALU Op: 2dup swap- ( n1 n2 -- n1 n2 n2-n1 )
  AND PUSH ALU Op: 2dup and ( n1 n2 -- n1 n2 n1_and_n2 )
  OR PUSH ALU Op: 2dup or ( n1 n2 -- n1 n2 n1_or_n2 )
  XOR PUSH ALU Op: 2dup xor ( n1 n2 -- n1 n2 n1_xor_n2 )

## Slide 7: uCore 1.20 Opcodes by Functionality
Complex Math Steps
  MULTS NONE ALU Op: mults ( u1 u2 -- u1 u3 )
  0DIVS NONE ALU Op: 0divs ( ud1 u2 -- u2 u3 )
  UDIVS NONE ALU Op: udivs ( u2 u3 -- u2 u3' )
  LDIVS NONE ALU Op: ldivs ( u2 u3 -- u2 u3' )
Stack manipulation
  DUP PUSH BRA Op: dup ( n -- n n )
  QDUP PUSH BRA Op: ?dup ( n -- n n | 0 )
  NEVER BOTH BRA Op: drop ( n -- )
  SWAPS NONE ALU Op: swap ( n1 n2 -- n2 n1 )
  NOS PUSH ALU Op: over ( n1 n2 -- n1 n2 n1 )
  NOS POP ALU Op: nip ( n1 n2 -- n2 )
  RSTACK BOTH MEM Op: r> ( -- n )
  RSTACK NONE MEM Op: >r ( n -- )
  TOR BOTH MEM Op: r@ ( -- n )
  TOR NONE MEM Op: r! ( n -- )

## Slide 8: uCore 1.20 Opcodes by Functionality
Registers
  STATUS BOTH MEM Op: status@ ( -- status )
  STATUS NONE MEM Op: status! ( status -- )
  RSP BOTH MEM Op: rsp@ ( -- rstack_addr )
  RSP NONE MEM Op: rsp! ( rstack_addr -- )
  DSP BOTH MEM Op: dsp@ ( -- dstack_ptr )
  DSP NONE MEM Op: dsp! ( dstack_ptr -- ? )
Data Memory access
  N PUSH MEM Op: +ld ( addr -- n addr+i )
  N POP MEM Op: +st ( n addr -- addr+i )
  LOCAL BOTH MEM Op: +lld ( i -- n rstack+i )
  LOCAL NONE MEM Op: +lst ( n i -- rstack+i )
  TASK BOTH MEM Op: +tld ( i -- n task+i )
  TASK NONE MEM Op: +tst ( n i -- task+i )

## Slide 9: uCore 1.20 Opcodes by Functionality
Exits
  ALWAYS NONE BRA Op: exit ( -- )
  ZERO NONE BRA Op: z-exit ( flag -- )
  NZERO NONE BRA Op: nz-exit ( flag -- )
  SIGN NONE BRA Op: s-exit ( -- )
  NSIGN NONE BRA Op: ns-exit ( -- )
  NOVL NONE BRA Op: no-exit ( -- )
  NCARRY NONE BRA Op: nc-exit ( -- )
Branches
  ALWAYS POP BRA Op: branch ( offset -- )
  ZERO POP BRA Op: z-branch ( offset -- )
  NZERO POP BRA Op: nz-branch ( offset -- )
  SIGN POP BRA Op: s-branch ( offset -- )
  NSIGN POP BRA Op: ns-branch ( offset -- )
  NOVL POP BRA Op: no-branch ( offset -- )
  NCARRY POP BRA Op: nc-branch ( offset -- )

## Slide 10: uCore 1.20 Opcodes by Functionality
Calls
  ALWAYS BOTH BRA Op: call ( offset -- )
  ZERO BOTH BRA Op: z-call ( offset -- )
  NZERO BOTH BRA Op: nz-call ( offset -- )
  SIGN BOTH BRA Op: s-call ( offset -- )
  NSIGN BOTH BRA Op: ns-call ( offset -- )
  NOVL BOTH BRA Op: no-call ( offset -- )
  NCARRY BOTH BRA Op: nc-call ( offset -- )
  QOVL PUSH BRA Op: ?ovl ( -- )
  N USR Op: user_call 32 uncommitted instructions
Complex Branches
  INT PUSH BRA Op: int ( -- status )
  IRET PUSH BRA Op: iret ( status -- )
  EXC PUSH BRA Op: exc ( -- )
  TIMES PUSH BRA Op: times ( n-1 -- )
  NEVER POP BRA Op: drop_flag ( flag offset -- offset )

## Slide 13: uCore instantiation for Geolon-MCS
Booting
FPGA Technology Issues

## Slide 15: The Interrupt and Exception Duality
Interrupt
  An event did happen that was not expected by software
Exception
  An event did not happen that was hoped for by software

## Slide 16: Time Services using Exceptions
Traditional Method using a Timer Interrupt
: ahead ( ticks -- time.ahead ) Timer @ + ;
: timeout? ( ticks -- ticks f ) dup Timer @ - 0< ;
: continue ( ticks -- ) BEGIN pause timeout? UNTIL drop ;
: sleep ( ticks -- ) ahead continue ;
Using an Exception
: continue ( ticks -- ) Timer ! ;
and now we can afford sub millisecond resolution as well

## Slide 17: Pseudo DMA
Transferring 16 bit data between IDE interface and Buffer memory
0 PUSH USR Opcode: ide@ ( bufaddr -- bufaddr+1 )
0 POP USR Opcode: ide! ( bufaddr -- bufaddr+1 )
and these types of instructions can be iterated using TIMES:
$FF times ide@
loads a sector into the buffer at one transfer/cycle plus 3 cycles overhead. Repeated instructions are fully interruptible without latency.

## Slide 18: Data Encoding and Buffering, soft encoded
(just appreciate its long winded complications)
: split ( 32b -- l16b h16b ) dup $FFFF and swap u256/ u256/ ;
: wsplit ( 16b -- l8b h8b ) dup $FF and swap u256/ ;
: buf8! ( 8bit -- )
>r idebuf_ptr @ 2/
carry IF ld swap r> 256* or swap !
ELSE r> $FF and swap !
THEN
idebuf_ptr ld swap 1+
dup [ #idebuf_top 2* ] literal u>
IF idebuf_flush drop #idebuf_addr 2* THEN
swap !
;
: buf16! ( 16bit -- ) wsplit buf8! buf8! ;
: buf24! ( 24bit -- ) split buf8! buf16! ;
: buf32! ( 32bit -- ) split buf16! buf16! ;
: abs ( n -- u ) neg IF 0 swap- THEN ;
: encode ( sample channel# -- )
under \ val val ch
samples + \ val val addr
ld >r swap r> ! \ val old store val in samples buffer
under - \ val difference
dup abs \ val difference |difference|
dup $40 < IF drop $7f and buf8!
drop EXIT
THEN
dup $1000 < IF drop $1FFF and $C000 or buf16!
drop EXIT
THEN
$80000 < IF $FFFFF and $E00000 or buf24!
drop EXIT
THEN
drop $7FFFFFF and $F0000000 or buf32!
;

## Slide 19: Data Encoding and Buffering, hardware supported
1 POP USR Opcode: buf8! ( 8b -- )
2 POP USR Opcode: buf16! ( 16b -- )
1 NONE USR Opcode: buf24! ( 24b -- 16b )
2 NONE USR Opcode: buf32! ( 32b -- 16b )
ENCODE NONE ALU Opcode: tag ( sample previous -- sample code )
: encode ( val ch# -- )
samples + ld >r tag
carry IF buf8! ELSE ovl IF buf32! THEN buf16! THEN
r> !
;
The core can be clocked at 1/4 speed, saving 20 mW.
The code is also more understandable and therefore, reliable beyond doubt©.

## Slide 20: uCore Scalability
CONSTANT data_width : NATURAL := 32;
CONSTANT data_addr_width : NATURAL := 21;
CONSTANT dcache_addr_width : NATURAL := 0;
CONSTANT prog_addr_width : NATURAL := 19;
CONSTANT pcache_addr_width : NATURAL := 0;
CONSTANT prog_ram_width : NATURAL := 16;
CONSTANT ds_addr_width : NATURAL := 6;
CONSTANT rs_addr_width : NATURAL := 8;
CONSTANT tasks_addr_width : NATURAL := 3;
CONSTANT interrupts : NATURAL := 2;

## Slide 21: uCore100 Prototyping Board
XC2S200 FPGA
256k x 8 program memory
256k x 32 data memory/return stack
User USB port
USB configuration port (to be programmed!)
Umbilical Interface
  Centronics
  RS232
Lots of uncommitted I/O pins

## Slide 22: uCore Licensing
uCore Exploratory License
  Equivalent terms to FreeBSD
My Business Interest
  tayloring instructions
  certifying compatibility with the original model

## Slide 23: Next Steps
Building a Development Community
GCC backend
Simulator for Windows/Linux
USB Programming Interface (8051no fun)
www.microcore.org